## Slide 1: 3D Slicer 2-Day Workshop
The George Washington University
4/1 & 4/3

## Slide 5: 3D Slicer Terminology
Scene – a project repository with a collection of data nodes
  Commonly saved as a .mrml or .mrb file
  This is the file you load up to resume a saved project
Node – any object or data set loaded into the scene (i.e., volume, segmentation, point list, etc.)
  When saving, you save the scene and the individual data nodes
Module – An independent “tool” that provides a set of functions for creating or manipulating data (i.e., Data module, Segment Editor module, Transforms module)
  3D Slicer comes with 100+ built-in modules with many more available to download
Extension – A collection of related modules that can be downloaded and installed into 3D Slicer using the Extensions module

## Slide 7
CT scanning – a method of combining x-ray imaging and computer technology to generate cross-sectional images of an object
Image Stack – a series of black and white cross-sectional images that contain computed-tomography data
  Common formats are standard image formats (.png, .jpg, .bmp, .tif ) or DICOM (.dcm)
Volume Node – image stacks are represented as a scalar volume node
  Saved as a .nrrd file
Voxel – a 3D pixel with XYZ dimensions
Image Spacing - the resolution of a CT scan; aka the XYZ dimensions of a voxel
  Needed to take accurate measurements from CT scans
Isotropy vs Anisotropy – isotropic data have the same image spacing in the XYZ directions; but when they differ the data is anisotropic
  Anisotropy in the Z dimension is common for a lot medical CT scans
Computed Tomograph (CT) Terminology

## Slide 8
Volume Rendering – a 3D visualization of the volume node
  Presets can be used to attribute grey-scale values with different colors
  Can NOT be saved as a 3D model; purely for visualization
Segmenting – the annotation of voxels to delineate structures
Segmentation Node – a data node that contains multiple segments, each of which typically represents a different structure
  Can be visualized in 3D, saved as a 3D model, and quantitatively analyzed
Model – a 3D surface representation of an object; in 3D Slicer it’s typically a representation of a segment
  Commonly saved as a .ply, .stl, or .obj – these formats are broadly applicable outside of 3D Slicer
  Models generated elsewhere can be loaded into Slicer (photogrammetry, CAD models, etc.) but BEWARE resolution
Computed Tomograph (CT) Terminology

## Slide 9: Workflow for computed tomography (CT) data
Image Stack
3D Slicer
Volume Rendering
Segmenting
Export to Model
Analyze
3D Printing
Linear Measurements
Segment Statistics
Landmarking for GMM
ImageStacks
Volume Rendering
Segment Editor
Segmentations;
Data
SlicerMorph;
Markups
Markups
Markups
Markups
Segment Statistics

## Slide 10
Resources
Downloading CT Scans
  Thousands of free scans on MorphoSource: https://morphosource.org
  How to download from MorphoSource: https://youtu.be/SWMketCDtGc?si=rcY9x6ajZ3BxfALv
Getting help with 3D Slicer
  3D Slicer Documentation: https://slicer.readthedocs.io/en/latest/index.html
  Tutorials by the SlicerMorph team: https://github.com/SlicerMorph/Tutorials/tree/main?tab=readme-ov-file
  3D Slicer Discourse Forum: https://discourse.slicer.org/